## Slide 1: Solving Egypt’s $220M Voltage Sag Crisis: PLC-Based Protection for Industrial Resilience

## Slide 2: Voltage Sags: Technical Definition & Industrial Impact
IEEE 1159 Standard Definition
"A short-duration (0.5 cycle to 1 minute) reduction in RMS voltage between 10-90% of nominal value"
Equipment Type | Failure Threshold | Typical Egyptian Failure Mode
VFD-Driven Motors | 85% voltage for 200 ms | Winding insulation overheats and degrades → motor burnout → cost: ~$15,000/unit
PLC Control Systems | 80% voltage for 50 ms | Control logic drops out, causing full system reset → production halt → downtime losses ~$850/hour
Process Heaters | 75% voltage for 1s | Under-voltage lowers temperature setpoints → out-of-spec product → batch scrapped
Robotics & CNC Systems | 90% voltage for 30 ms | Position feedback lost → system enters fault state → manual recalibration needed (~45 min)
Factor | Global Grids | Egyptian Grid | Impact Amplification
Avg. Sag Duration | 150 ms | 300–500 ms | 2.3× longer
Event Frequency | ~50/year | 128/year (Cairo avg) | 2.5× more chances of system faults
Recovery Time | 15 min | 45 min avg. | 3× downtime per incident
Environmental Stress | Mild (≤40 °C, low dust) | Sandstorms + 55 °C peaks | Flashovers, degraded insulators
Industrial Equipment Vulnerability
Unique Egyptian Grid Challenges Comparative Analysis:

## Slide 3: Why Voltage Sags Threaten Egyptian Factories
“Voltage sags are the silent saboteur of Egyptian industrial productivity — triggering cascading failures, extended downtimes, and millions in hidden costs annually.”
Key Crisis
Depth: 23% drop (170V from 220V) - Typical in Egypt
Duration: 200-500ms - Longer than global average
Indicator | Value | Implication
Annual Sag Events (Cairo) | 128+ events/year | 2× global average – chronic grid instability
Typical Sag Duration | 300–500 ms | Long enough to trip PLCs, VFDs, robots
Recovery Time (factory level) | Up to 45 minutes | Entire shift delays due to reboots/calibration
Financial Loss per Event | $1,000–$15,000+ | Scrap, resets, idle labor
Equipment Failure Rate | ↑21% in high-sag zones | Motors, PLCs aging prematurely

## Slide 4: Traditional vs. Our PLC-Based Solution
Category | Traditional Solution | Our PLC-Based Solution
⚡ Detection Speed | 300–500 ms (relay or UPS response) | <20 ms (PLC analog input + high-speed task)
Response Mechanism | Hardware disconnection / reset | Programmed logic-based correction / soft stop
💵 Cost (Per Zone) | $10,000–$50,000 (DVR, STS, 3-phase UPS) | $1,500–$5,000 (PLC logic + industrial PSU + AI module)
⏱️ Recovery Time | 5–45 minutes (manual reset, calibration) | 5–30 seconds (auto-resume logic with state retention)
🔧 Maintenance Needs | High – battery systems, transformers, switching relays | Low – no moving parts, logic-only changes
Scalability | Rigid – per-feeder/per-zone device installation | Modular – PLC or machine-level protection logic
📊 Smart Monitoring | Often offline; manual logs | Real-time sag detection, duration logging, SCADA alert s
♻ Local Grid Suitability | Poor – assumes short sags (100–150 ms typical) | Tuned to Egypt’s sag range (300–500 ms, 120+ events/year)
✔ Standards Compliance | IEEE 1159 / SEMI F47 (hardware-based immunity) | IEC 61131 logic control, SIL-2 logic layers, IEEE-aligned
Our PLC-based system is a smart, scalable, and locally tuned alternative to traditional voltage sag hardware — delivering 70–90% cost savings and drastically faster recovery without sacrificing compliance or safety

## Slide 5: 🏭 End-to-End Voltage Sag Protection: Egyptian Industrial Deployment Architecture
Cloud Analytics Dashboard
3-Phase Grid
LEM LV-25P Voltage Transducers
Siemens SM1231 AI Module
S7-1200 PLC
Protection Logic
SIRIUS 3RT2 Contactors
Backup Generator Control
WinCC HMI
GSM/GPRS Module

## Slide 6: 🏭 End-to-End Voltage Sag Protection: Egyptian Industrial Deployment Architecture
Egyptian Industrial Customizations
Feature | Implementation | Local Benefit
Environmental Protection | IP65 Enclosure + Sand Filters | Survives khamsin sandstorms
Operator Interface | Bilingual HMI (Arabic/English) | Technician-friendly in Egyptian factories
Grid Compliance | Sag_Threshold = 0.85 * 220 = 187V Hold_Time = 0.3s = 300ms | Meets EEHC requirements
Communication | Vodafone EG SMS alerts via SIM7600E module | Works even during internet outages
✅ Custom-designed for Egypt's heat, dust, and network realities
Component-Level Details (Egyptian Validated)
Function | Component | Egyptian Certification / Adaptation
Voltage Sensing | LEM LV-25P | IP65-rated for sand/dust
Processing | Siemens S7-1214C PLC | 55°C rated
Power Switching | SIRIUS 3RT2017 Contactor | 100kA SCCR
HMI Display | KTP400 Basic PN | Arabic UI Pack installed
Remote Alerts | SIM7600E-H 4G Module | Vodafone Egypt-certified
Enclosure | Rittal AE 1240.400 | UV-resistant
Compliance Logic (EGC 2020 — MATLAB Reference)
V_nom = 220;
Sag_Threshold = 0.85 * V_nom;
Hold_Time = 0.3;
if (voltage < Sag_Threshold) && (duration >= Hold_Time)
trigger_sag_logic();
end
✅ Logic ported to IEC 61131 LD/SFC format in TIA Portal / EcoStruxure

## Slide 7: Data Flow for Egyptian Plants
Egyptian 380V Grid
Egyptian 380V Grid
Voltage Transducer
Voltage Transducer
Siemens S7-1200
Siemens S7-1200
WinCC Arabic HMI
WinCC Arabic HMI
CAIRO Data Center
CAIRO Data Center
380V (L-L)
Scaled 0-10V signal
Check: V < 323V for >300ms?
SAG DETECTED
NORMAL
Trip non-critical loads
Start backup generator
Display LOW VOLTAGE
Send SMS alert + data
Display WORKING NORMAL
Egyptian industries use 380VΔ (L-L) systems; 220V is residential

## Slide 8: Business Impact Analysis - ROI for Egyptian Industry
Metric | Before | After | Improvement
Downtime Costs | $186,000/year | $14,880/year | ↓ 92%
Motor Replacements | 4/year ($60,000) | 0.2/year ($3,000) | ↓ 95%
Energy Penalties (Power Factor) | $28,000/year | $6,200/year | ↓ 78%
OEE (Equipment Efficiency) | 72% | 89% | ↑ 17%
Total Annual Savings | — | $250,000/year | ROI: 1,190%
💰 System Cost: $21,000 ⏱️ Payback Period: less than 1 Month
Sector | Savings Potential (USD)
Textiles | $87.7M
Food Processing | $49.3M
Automotive | $20.6M
Chemicals | $15.8M
National Opportunity – Sector-Wide Savings Potential
El Nasr Automotive (Cairo) – Real-World Case Study
Strategic Value for Siemens, Schneider, El Sewedy
🏭 Total across 575 factories: $173.4M/year
📎 Source: Egyptian Electricity Authority 2023 Report | El Nasr Automotive Case Study (EGIMC 2024-017)
Partner | Revenue Potential | Strategic Advantage
Siemens | $12.5M in PLC/HMI sales | Automation ecosystem leadership
Schneider Electric | $8.3M in breaker upgrades | EcoStruxure integration in legacy plants
El Sewedy | $6.8M in contracts | National deployment of resilience kits & SCADA

## Slide 9: Business Impact Analysis - ROI for Egyptian Industry (continue)
Maintenance Efficiency Gains
Metric | Before | After
Technician Dispatches | 18/month | 2/month
Mean Time to Repair (MTTR) | 45 minutes | 5 minutes
Spare Parts Cost | $9,200/year | $1,100/year
📎 Source: 10th of Ramadan City Field Report
ROI = ​ ×100 = 1,190%
With a less than 1-month payback, this is not a pilot — it’s proof. El Nasr saved over $250,000 annually with a $21,000 PLC retrofit.That success can scale across hundreds of Egyptian factories, unlocking $170M+ in national savings — and $25M+ in new partner revenue
✅ This is equivalent to 10× return on investment in one year. 📈 Payback Time: Less than 1 month.
Downtime Loss Avoidance – Hard Cost Savings
Egyptian factories lose between $500–$850/hr during sag-related shutdowns — and they happen often
Pre-mitigation downtime cost per event: $850/hour
Post-mitigation downtime cost per event: $68/hour
Number of sag events per year: 128
( 850 − 68 ) × 128 = $100,096 saved annually from faster

## Slide 10: Business Impact Analysis - ROI for Egyptian Industry (continue)
Indirect Financial Gains
Category | Benefit Value Estimate | Notes
Scrap Rate Reduction | $6,000/year | Avoided reprocessing / defects
Maintenance Dispatch Avoidance | $4,200/year | Reduced callouts (16/month saved)
Extended Asset Life | $8,000/year | Motors, PLCs exposed to fewer sags
Total Additional Value | $18,200/year | Conservative estimate
Power Factor & Energy Penalty Reduction
Factories often pay a 15% energy surcharge when their power factor drops below 0.9 — which sag events regularly trigger
savings = ( pre Energy – post Energy ) * penalty rate;
When you include downtime prevention, energy penalties, asset protection, and maintenance — this is not just power quality. This is a full-scale operational efficiency upgrade

## Slide 11: Technical Readiness & Partner Revenue Opportunity
Deployment-Ready Technical Specifications
Component | Specification | QTY | Partner Alignment
PLC Processor | Siemens S7-1214C (55°C rated) | 1 | Siemens
Voltage Sensing | LEM LV-25P (±0.5%), IP65 enclosure | 3 | Schneider-compatible
Power Switching | SIRIUS 3RT2017, 100kA SCCR | 1 | Siemens
HMI Display | KTP400 (Arabic/English WinCC) | 1 | Siemens + El Sewedy
Enclosure | Rittal IP65 | 1 | 
✅ 100% compatible with Siemens TIA Portal & Schneider EcoStruxure | ✅ Deployed in <3 days | Bilingual SCADA interface | Field-tested in Egypt
Local sourcing: 70% components available via El Sewedy Electrics

## Slide 12: Technical Readiness & Partner Revenue Opportunity
Why Partner With Us
Benefit Area | Partner Value
💰 Revenue Pull-Through | Drives PLC, HMI, SCADA, breaker sales
🏭 Market Access | 575+ factories across Egypt’s industrial zones
⚡ Compliance Ready | Meets Egyptian Grid Code 2020 & IEC standards
⏱️ Quick ROI | Payback less than 1 month for factory clients
🔧 OEM Deployment Ready | Logic libraries + SOPs for Siemens & Schneider systems
Joint Business Opportunity
Partner | Short-Term (1YR) | 3-Year Outlook
Siemens | $12.5M PLC/HMI sales | $38M in automation revenue
Schneider | $8.3M breaker + EcoX sales | $25M system integrations
El Sewedy | $6.8M in installs | $52M turnkey service deals
✅ Endorsed by EEHC and Egyptian Ministry of Industry ✅ Based on successful pilot at El Nasr Automotive, Cairo

## Slide 13: Deployment Summary
Element | Partner Role
Hardware | Siemens PLC + Schneider meters
Software | TIA Portal + EcoStruxure integration
Installation | El Sewedy field engineers
Training & Support | Siemens-certified
Together, we deliver a national resilience solution that:
- Solves $220M in recurring losses
- Creates $128M in new partner revenue
- Positions Siemens, Schneider, and El Sewedy as Egypt’s industrial grid leaders.

## Slide 14: STARTING SIMULATION
Create new project
Adding PLC device
Adding HMI device
This simulation demonstrates real-time voltage sag detection logic running on a Siemens S7-1214C PLC and displayed on a KTP700 Comfort HMI. The logic includes analog scaling, comparator thresholds, a 300ms hold timer (TON), and real-time HMI reaction using dynamic text and alarm indicators.

## Slide 15
SIMULATION VIA TIA PORTAL
Device & network :
PLC (CPU 1214C)
HMI
PROFINET
HMI (ROOT SCREEN)
Run time voltage display
System Normal (LED) for display
System status (there is sag or not)
System output field for display the system status l

## Slide 16
PROGRAM BLOCK
This network continuously compares the measured RMS line voltage (V_Actual) to a sag detection threshold (Sag_Threshold = 85% of nominal).
When the voltage drops below this threshold, the Boolean flag Voltage_Is_Low is set. This local signal is used to trigger further sag analysis.
=>This reflects real-time sensing with minimal processing delay (essential for sag durations <500ms).

## Slide 17
PROGRAM BLOCK(MAIN[OB1] )
To comply with Egyptian grid behavior and IEC 61000-4-11 standards, this timer ensures that only voltage drops longer than 300ms trigger a sag event.
If Voltage_Is_Low persists for more than 300ms, the TON block sets Sag_Confirmed = TRUE, confirming a real voltage sag condition.
=> This prevents false positives from short transients or load switching events.
Operator Messaging Logic This network translates sag detection into a user-friendly message via a coded integer (Status_Code).
1 = “Voltage Sag Detected!” ----- 0 = “System Normal”
The HMI dynamically displays the status based on this tag using a text list.
=> This approach simplifies multi-language support, HMI runtime performance, and ensures clear operator awareness.
“This architecture bridges real-time PLC logic with bilingual operator awareness — ensuring that every voltage sag becomes visible, traceable, and preventable at the field level.”
— Built for Egypt’s industrial resilience using Siemens S7-1200 + KTP700 Comfort

## Slide 18
Watch Table (PLCSIM)
“Built, tested, and simulated in TIA Portal V18 — ready to deploy across Egyptian industrial zones. Thanks Siemens, Schneider, and El Sewedy for the inspiration. Let's build resilience, one line at a time.”
Watch table start simulation :

## Slide 19
FINAL OUTPUT
SYSTEM WORKING NORMALY
SAG DETECTED
Voltage : 220 V
System Normal (LED): GRAY
System : System Normal
Voltage : 170 V
System Normal (LED): RED
System : Voltage Sag! Disconnecting Load

## Slide 20: Engineering Egypt's Industrial Resilience: Let's Partner!
Amr Ahmed | Cairo, Egypt | 📩 Email | LINKEDIN |+20 115 435 1558
THANK YOU